1. Need a USB to TTL serial port module（CH340, FT232, etc…）

1. Download the bootloader

The file I sent you:  bootloader.hex

2. Download and install the burning software :FlashMagic

http://www.flashmagictool.com

3. Insert the boot pin on the main board into the jumper cap, the wiring between the usb to ttl module and the skr V1.4 main board is shown in the figure below, the GND of the module is connected to the GND of the main board, the TX of the module is connected to the RX of the main board, and the RX of the module is connected to the main board TX.

4. Power on the motherboard, insert the usb to ttl module into the computer, open the FlashMagic downloaded and installed in step 2, go to the device manager, find the port number used by the usb to ttl module, as shown on the left side of the figure below, the port number is COM96, in FlashMagic, set the COM Port where ① in the picture is located to COM96, select the file to be burned in ② as the bootloader we downloaded in step 1, check other settings of FlashMagic, if it does not match the picture, please change it to To be consistent with the picture, click ③Start to start burning. After burning, pull out the boot jumper, and then power on again to update the firmware named "firmware.bin".